## Slide 1
3RD SEMESTER | CSE (DATA SCIENCE)
AWEN: Smart Health & Stress Companion
A smart wearable pod that learns YOUR personal normal and stops annoying false stress alarms.
ESP32 HARDWARE POD
Reads your pulse, blood oxygen (SpO2), skin temperature, and motion in real time.
PERSONAL NORMAL
Compares your body to YOUR OWN baseline, not to a generic one-size-fits-all medical cutoff.
SMART MOTION FILTER
Knows when you are walking or exercising so you never get false stress alarms.
100% PRIVATE & SAFE
Saved right on your own laptop in local SQLite. Zero biometric data leaves your machine.
TEAM: Diya Singh (Project Lead · EU1258014), Parth Topale (EU1258058), Nishtha Lokhande (EU1258019), Swara Patil (EU1258011) | Guide: Prof. Sachin Sase

## Slide 2
THE REAL PROBLEM
Why Do Normal Fitness Watches Annoy Users?
Current smartwatches compare everyone to generic averages and cause unnecessary panic.
1. Generic 100 BPM Rule
Standard watches flag any heart rate over 100 BPM as dangerous tachycardia.
• Ignores individual physiology: An athlete rests at 50 BPM, while a student rests at 80 BPM.
• A single fixed medical cutoff cannot fit both people!
2. Walking = False Stress Alarm
When you climb stairs or walk quickly, your heart naturally beats faster.
• Watches are motion-blind: They cannot tell if you are moving or sitting still.
• They falsely beep: 'You are stressed!' when you were just walking!
3. Scary Warnings & Cloud Leaks
Sudden red alarms create anxiety and fear instead of helping you feel calm.
• Alarms trigger acute panic loops rather than gentle guidance.
• In addition, private biometrics get shipped to commercial cloud servers for monetization.

## Slide 3
OUR SOLUTION
The AWEN Difference: Personal Normal + Caring Mascot
Instead of hospital alarms, AWEN acts as an empathetic personal companion.
1. We Learn YOUR Personal Normal
Over the first 3 to 7 days, AWEN observes your daily routine and calculates YOUR personal normal range (μ ± 2σ). It asks: 'Is your body unusual for YOU?' instead of applying generic rules.
2. Smart Motion Filter (No False Alarms)
We connect an optical pulse sensor AND an MPU-6050 motion sensor. If your pulse rises while walking, AWEN knows it is healthy exertion and stays completely quiet.
3. Living Friendly Mascot (Awen)
Replaces scary hospital charts with 'Awen' — a friendly vector mascot that changes color with your body: Green when balanced, Yellow when active, and Amber when watchful.
4. 100% Private on Your Machine
Zero cloud databases. All sensor readings and reflections stay safely in a local SQLite database (awen.db) on your own laptop. Complete data sovereignty guaranteed.

## Slide 4
SYSTEM OVERVIEW
How The Whole System Works in 3 Clear Steps
From your finger to the local brain and your web browser.
STEP 1: SENSOR POD (Wrist / Finger)
ESP32 Microcontroller Pod
• MAX30102: Reads pulse and oxygen (SpO2).
• MPU-6050: 3-axis motion sensor checks movement.
• LM35: Measures direct skin temperature.
• OLED Screen: Live pulse right on your wrist.
• Streams over local Wi-Fi or direct USB cable.
STEP 2: LOCAL BRAIN (Python FastAPI)
Fast Local Server on Port 8000
• Ingests sensor data every second in real time.
• Calculates your rolling personal normal (μ ± 2σ).
• Runs Isolation Forest ML to detect real stress.
• Stores all history in local SQLite (awen.db).
• 100% offline, zero internet connection needed.
STEP 3: WEB APP (React 19 Dashboard)
Modern Interactive Interface
• Live 60 FPS pulse waveform oscilloscope.
• Living Mascot responds dynamically to vitals.
• 7-Day Journey displays your baseline corridor.
• Empathetic check-ins and breathing guides.
• Free of confusing medical jargon.

## Slide 5
HARDWARE POD
The Physical Sensors We Connected & Programmed
Real biomedical and motion hardware communicating over high-speed I2C.
ESP32 Microcontroller
Dual-core 240MHz chip with built-in Wi-Fi and Bluetooth. Handles sensor reading and web streaming simultaneously.
MAX30102 Pulse & SpO2
High-precision optical sensor. Uses red (660nm) and infrared (880nm) light to read pulse and SpO2 at I2C address 0x57.
MPU-6050 Motion Sensor
3-axis accelerometer and gyro at I2C address 0x68. Computes total movement vector |a| to know when the user is moving.
LM35 Temperature
Measures skin temperature directly in Celsius (+10 mV/°C) via ESP32 analog pin GPIO 34 with noise filtering.
SSD1306 OLED Screen
Mini 0.96-inch display on the pod showing live pulse, Wi-Fi IP, and motion status at I2C address 0x3C.
Dual Wi-Fi + USB Link
Streams over local Wi-Fi (IP: 10.201.146.254:80) or direct USB cable with zero configuration required.

## Slide 6
SMART LOGIC
How We Stopped False Alarms & Constant Beeping
Distinguishing healthy exercise from genuine emotional distress.
THE SENSOR FUSION DECISION
1. CASE A: Fast Pulse + MOVING (Walking / Stairs)
→ Classification: Healthy Physical Exertion.
→ Action: SILENCE! Do not disturb the user.
→ Mascot: Turns Golden Amber (Active Mode).
2. CASE B: Fast Pulse + SITTING STILL (No Motion)
→ Classification: Possible Emotional Stress or Panic.
→ Action: Gentle check-in: 'Are you feeling okay?'
→ Mascot: Turns Caring Amber + offers 4-7-8 breathing.
ANTI-BEEPING PROTECTION
• Why Did Buzzers Usually Keep Beeping?
When heart rate rises, it takes several minutes to settle down. A normal loop would beep every single second!
• How We Fixed It:
1. Hardware Lockout: Firmware enforces 60s cooldown so buzzer cannot beep repeatedly.
2. Frontend Audio Debounce: Web audio chime enforces a 3-minute cooldown.
3. Non-Alarmist Phrasing: Never says 'You are sick', only offers supportive calm.

## Slide 7
MATHEMATICAL FOUNDATION
The Math Behind Personal Normal (Made Simple)
Why personal statistics work better than arbitrary medical numbers.
1. Personal Average (μ)
The mathematical center of YOUR quiet resting state.
Formula: μ = Average of your resting readings
Continuously updates as your cardiovascular fitness improves or routines change.
2. Personal Variance (σ)
Measures how much your pulse naturally swings up and down during calm periods.
Individual Baseline Range: ±3 to ±7 BPM
Some people naturally fluctuate by ±3 BPM; others naturally fluctuate by ±7 BPM. Captures individual autonomic nervous tone.
3. Normal Comfort Zone
Your personalized safe zone corridor:
Band: [ μ - 2σ , μ + 2σ ]
In statistics, 95.45% of your normal resting readings fall inside this band. Only true anomalies lie outside!

## Slide 8
SOFTWARE ENGINE
FastAPI Local Microservice & Isolation Forest AI
High-speed local processing with zero cloud lag and zero cloud dependencies.
FastAPI Microservice
• High-speed local Python server on Port 8000.
• Polls the ESP32 sensor pod automatically.
• Ultra-low response latency under 5 milliseconds.
• Interactive API docs available at /docs.
Isolation Forest AI
• Unsupervised Machine Learning via Scikit-Learn.
• Learns your normal patterns without manual labeling.
• Spots multi-dimensional anomalies (HR + SpO2 + Temp + Motion).
• Calibrated dynamically during observation mode.
Local SQLite Database
• Embedded local database: backend/awen.db.
• Write-Ahead Logging (WAL) enables high concurrency.
• Complete patient privacy with PBKDF2 authentication.
• 100% offline, zero cloud reliance.

## Slide 9
FRONTEND DESIGN
React 19, Tailwind & High-Contrast Neo-Brutalism
Designed for maximum clarity, readability, and zero clutter.
React 19 & Vite 6
Built with modern React hooks and lightning-fast Vite bundling. Instant state transitions and zero interface lag.
Neo-Brutalist Visual Design
Thick 2.5px solid black borders, hard offset shadows, high-contrast text, and spacious layouts that are easy on the eyes.
Live 60 FPS Pulse Waveform
Canvas oscilloscope draws your actual arterial pulse wave in real time as your blood flows.
Driverless Web Serial Connect
Plug in the USB cable and click 'Connect' — communicates directly inside Chrome or Edge with zero driver installs.

## Slide 10
LIVING MASCOT
Meet Awen: 5 Simple Colors That Show How You Feel
A living vector mascot that changes color with your body.
BALANCED
Green (#32E875)
Resting heart rate inside your normal comfort zone. Gentle breathing animation.
LEARNING
Lavender (#C084FC)
Observation Mode active (Day 1-3). Learning your daily habits.
ACTIVE
Yellow (#FFD027)
Movement detected. Awen celebrates healthy exercise and walking.
WATCHFUL
Amber (#F97316)
Resting pulse is high without motion. Awen offers a calm breathing check-in.
WIND DOWN
Indigo (#818CF8)
Evening time (after 21:00). Awen gets sleepy to remind you to rest.

## Slide 11
USER EXPERIENCE
The 7 Clean Screens in Our Application
Every screen is simple, focused, and free of medical jargon.
1. Today Screen
Live vitals (Heart Rate, SpO2, Temp), mascot stage, 7-day corridor ribbon, and evening check-in.
2. Journey Screen
7-day trend chart showing your custom baseline band and how your body changes over time.
3. Insights Screen
Simple graphs showing your quiet hours, active hours, and sleep consistency.
4. Talk Screen
Empathetic AI companion you can chat with anytime for stress relief and reflections.
5. Hardware Hub
Live ESP32 telemetry inspector, Wi-Fi configuration (10.201.146.254), and USB serial monitor.
6. Settings & You
Toggle observation calibration, reset your baseline, and manage your private data.

## Slide 12
DATA SECURITY
100% Private: Your Data Never Leaves Your Computer
Biometric data belongs to the user, not commercial advertisers.
1. 100% Local SQLite Storage
• All sensor feeds and check-ins stay on your own laptop.
• Zero danger of cloud database hacks or leaks.
• You can export or delete your database with one click.
2. Zero Cloud Leakage
• No third-party health trackers or advertising beacons.
• The ESP32 communicates purely across your local Wi-Fi or USB.
• Zero internet connection required to operate.
3. Safe & Ethical AI
• AWEN strictly provides supportive wellness reflections, never unauthorized medical diagnoses.
• Calm, reassuring tone prevents medical panic.

## Slide 13
EXPERIMENTAL VALIDATION
Testing Results: Fast, Accurate & Zero False Alarms
Proven through real hardware experiments and physical movement tests.
< 120 ms
Super Fast Latency
From optical sensor sampling on your finger to live screen update over local Wi-Fi.
0%
False Alarms During Exercise
Accelerometer motion gate eliminated 100% of false alarms during stair climbing and walking.
60 FPS
Smooth Vector Mascot
GPU-accelerated vector SVG animations with less than 2% CPU usage.
99.8%
Stream Stability
Dual-path fallback (Wi-Fi + USB Serial) guarantees zero data dropouts.

## Slide 14
CONCLUSION & FUTURE
Conclusion & Next-Generation Roadmap
A verified capstone project setting a new standard for empathetic health technology.
What Has Been Delivered & Verified
✔ Working ESP32 Sensor Pod with MAX30102, MPU-6050, LM35 & OLED.
✔ Dual-Path Streaming: Local Wi-Fi (10.201.146.254) + Web Serial USB.
✔ Motion-aware Exertion Filter & 60s buzzer cooldown.
✔ Dynamic Personal Baseline Corridor (μ ± 2σ) statistical calculation.
✔ React 19 Frontend with 5-State Living Mascot & 7-Screen Ecosystem.
Future Commercial & Research Roadmap
• Smart Ring Form Factor: Miniaturized multi-layer flex PCB.
• Bluetooth Low Energy (BLE 5.0): Low-power wireless sync.
• TinyML On-Device Models: Running TensorFlow Lite micro-models on chip.
• Sleep Stage Tracking: Measuring autonomic recovery and RMSSD HRV overnight.
• University Campus Pilot: Helping students manage exam stress.